Hellenic Accreditation System

| Annex F2/9 to the Certificate No. 972-4 SCOPE of ACCREDITATION of the Calibration Laboratory of Measurement Technology O.E. - Expertech |
| --- |
| Measurand / Calibration item | Range of measurement | Calibration & Measurement Capability (k=2)* | Remarks |
| Volume measurements |
| Liquid Volume / - Fixed metal tanks - Fixed metal cylindrical tanks for alcoholic beverages | [0,1 m3 to 0,5 m3) | 0,17 % | Volumetric method using flow meter according to ISO 4269:2001 Calibration medium: tap water. Calibration is performed on site. |
|  | [0,5 m3 to 400 m3] | 0,10 % |  |
| Liquid Volume / Road tankers | 0,5 m3 to 50 m3 | 0,10% | Volumetric method using flow meter according to: ISO 4269:2001 OIML R80-2:2017, Annex B Calibration medium: tap water. Calibration is performed on site. |

* Where uncertainty is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative. All uncertainties refer to the nominal tank volume.

Site of assessment: Permanent laboratory premises, 8th km Marathonos Ave. & Argonafton, 15351 Pallini, Greece

Approved Signatories: N. Lampis, S. Smirnios

This scope of Accreditation replaces the previous one dated 21.03.2023.

The Accreditation Certificate No. 972-4, to ELOT ΕΝ ISO/IEC 17025:2017, is valid until 1.04.2028.

Athens, 23.06.2023

Christos Nestoras

CEO of ESYD