Hellenic Accreditation System

Annex F1/X17 to the Certificate No. 142-5 SCOPE of ACCREDITATION οf the Department of Chemical Services of Rhodes of the Chemical Service of Aegean of the General Chemical State Laboratory

| Tested materials/ products | Types of test/ Properties to be measured | Applied Methods/ Techniques to be used |
| --- | --- | --- |
| Chemical tests |
| 1. Drinking, surface and underground water 1. Drinking, surface and underground water (cont.) | 1. Determination of Na+, K+, Ca2+, Mg2+ cations | In-house method, using ion chromatography, based on ELOT EN ISO 14911:2000 Method code: ΜΕΘ 64 10 02 |
|  | 2. Determination of F-, Cl-, NO2-, NO3- PO43-, SO42-, Br- anions | In-house method using ion chromatography, based on APHA 4110Β and ΕLOT ΕΝ ISO 10304.01:2010 Method code: ΜΕΘ 64 10 03 |
|  | 3. Determination of conductivity | APHA 2510 B Method code: ΜΕΘ 64 10 04 |
|  | 4. Determination of hardness | APHA 2340 C Method code: ΜΕΘ 64 10 05 |
|  | 5. Determination of pH | APHA 4500-Η+ Β Method code: ΜΕΘ 64 10 06 |
|  | 6. Determination of metals: Cr, Mn, Cd, Pb, Ni, Cu, Fe, Αs, Sb | In -house method using atomic absorption spectroscopy, based on APHA 3113 and USEPA method 200.9, Rev. 3, 1998. Method code: ΜΕΘ 64 10 07 |
|  | 7. Determination of Hg | In-house method using atomic absorption spectroscopy-hydride technique, based on APHA 3114C Method code: ΜΕΘ 64 10 24 |
| 2. Drinking, surface and ground water | 1. Determination of free and total (after distillation) cyanide | In-house method using ion chromatography and amperometric detector, based on APHA 4500-CN.C Method code: ΜΕΘ 64 10 23 |
| 3. Surface water and treated sewage | 1. Determination of chemical oxygen demand (COD) | In house method using photometry based on ISO 15705:2002. Method code: ΜΕΘ 64 10 20 |
| 4. Surface water and treated sewage | 1. Determination of biochemical oxygen demand (BOD5) | In-house method based on APHA 5210 D. Method code: ΜΕΘ 64 10 21 |
|  | 2. Determination of total suspended solids (TSS) | ISO 11923:1997 Method code: ΜΕΘ 64 10 22 |
| 5. Bottled water and drinking disinfected water | 1. Determination of bromate ions | In-house method using ion chromatography, based on ELOT EN ISO 11206:2014 Method code: ΜΕΘ 64 10 01 |
| 6. Alcohol and spirit drinks and wines | 1. Determination of alcoholic strength | E.E.C. 2870/2000 C43/19-2-2010 OIV-MA-AS312-01A:R2009 by electronic densimetry Method code: ΜΕΘ 64 10 12 |
| 7. Alcohol, alcoholic beverages and distillates | 1. Determination of volatile components: methanol, acetaldehyde, 1-propanol, acetic ethyl ester, 1- and 2-butanol, isobutanol, isoamyl alcohol | Regulation EC/2870:2000. Method code: ΜΕΘ 64 10 13 |
| 8. Beer, malt extract | 1. Determination of alcoholic strength and density | In-house method using density meter and alcoholic meter (NIR) Method code: ΜΕΘ 64 10 11 |
|  | 2. Determination of alcoholic strength w/w, plato w/w., plato w/v., extract w/w., degree of fermentation | In-house method Method code: ΜΕΘ 64 10 11 |
| Microbiological tests |
| 1. Drinking, sea, swimming and surface water | 1. Enumeration of intestinal enterococci | ISO 7899-2:2000. Method code: ΜΕΘ 64 10 15 |
|  | 2. Enumeration of coliforms and E. coli | ISO 9308-1:2014 Method code: ΜΕΘ 64 10 14 |
| 2. Drinking water | 1. Enumeration of the sum of vegetable cells and spores of Cl. perfringens | ISO 14189:2013 Method code: ΜΕΘ 64 10 16 |
|  | 2. Enumeration of culturable micro-organisms at 22(C and 36(C | ISO 6222: 1999 Method code: ΜΕΘ 64 10 18 |
|  | 3. Enumeration of Pseudomonas aeruginosa | ISO 16266:2006 Method code: ΜΕΘ 64 10 17 |
|  | 4. Enumeration of Legionella spp. | ISO 11731:2017 (§8.4.3.1) Method code: ΜΕΘ 64 10 19 |

Site of assessment: Laboratory permanent premises, Gabriel  Haritou Square 17, 85131 Rhodes.

Approved signatories: V. Matsis, M. Lachaniati, P. Triandafyllou, Z. Masen.

This Scope of Accreditation replaces the previous one dated 1.11.2023.

The Accreditation Certificate No. 142-5, according to ELOT EN ISO/IEC 17025:2017, has been extended until 06.11.2024.

Athens, 02.05.2024

Christos Nestoras

CEO of ESYD