Hellenic Accreditation System

Annex F1/17 to the Certificate No. 418-5 SCOPE of ACCREDITATION of the Testing Laboratory of ALEXANDER ELIA PAPADOPOULOS-I.C.Lab.

| Materials / Products to be tested | Types of test / Properties to be measured | Applied methods / Techniques to be used |
| --- | --- | --- |
| Electrical tests |
| Transformer insulating oils | Breakdown voltage (BDV) | IEC 60156:2018 (Ed.3.0) ASTM D1816-12(2019) |
| Physical tests |
| Transformer insulating oils Lubricants | Interfacial tension (IFT) | ASTM D 971-20 |
|  | Dynamic and calculation of kinematic viscosity at 40oC (V40) | ASTM D7042-21 |
|  | Dynamic and calculation of kinematic viscosity at 100oC (V100) | ASTM D7042-21 |
|  | Density (D) | ASTM D7042-21 |
|  | Viscosity index calculation (VI) | ASTM D7042-21 |
|  | Visual color determination (C) | ASTM D1500-12(2017) |
|  | Flash Point (FP) | ASTM D3828-16a. |
| Materials / Products to be tested | Types of test / Properties to be measured | Applied methods / Techniques to be used |
| Chemical tests |
| Transformer insulating oils Lubricants | Water content (WC) | ASTM D 1533-20 |
|  | Polychlorinated biphenyls (PCBs) | ASTM D 4059-00 (Reapproved 2018) |
|  | Acid number (AN) | ASTM D 974-14e2 |
|  | Analysis of Gases Dissolved in Electrical Insulating Oil by Gas Chromatography (DGA) | ASTM D3612-02 (Reapproved 2017) IEC 60567:2011(Ed.4.0) |
|  | Furanic Compounds in Electrical Insulating Liquids by High-Performance Liquid Chromatography (Fur-HPLC) | ASTM D5837-15 IEC 61198:1993 (Ed.1.0) |
|  | Corrosive Sulfur in Electrical Insulating Oils (CS) | ASTM D1275-15 |
|  | Examination of insulating oils in the infrared (FTIR) | ASTM D2144-07(2013) |
|  | Determination of dibenzylsulfide (DBDS) | IEC 62697-1 (2012). |
|  | Phenolic oxidation inhibitors (antioxidants DBP & C) | ASTM D2668-07(2013) IEC 60666:2010-A&B. |
|  | Determination of passivators in mineral oils (Pass) | IEC 60666:2010-Annex B. |
| Liquid Waste | Mercury (Hg) | EPA 7473-07 |
| Samplings |
| Transformer insulating oils | Sampling | IEC 60475:2011 (Ed.2.0) ASTM D 923-15 |
| Opinions and Interpretations |
| Transformer insulating oils | Interpretation of laboratory results using the accredited methods on samples of transformer insulating oils and expression of opinions on sample state and the operational state of the insulated equipment | In-house method based on IEC 60296, IEC 60422 and IEC 60599:2015 |

Site of assessment: Permanent laboratory premises, 16A Persefonis Str., Elefsina, Attiki, Greece.

Approved signatory: Alexander E. Papadopoulos.

This Scope of Accreditation replaces the previous one dated 12.05.2021.

The Accreditation Certificate No. 418-5, to ELOT EN ISO/IEC 17025:2017, is valid until 08.11.2024.

Athens, 04.04.2024

Christos Nestoras

CEO of ESYD