#### Hellenic Accreditation System

Annex F2/7 to the Certificate No. 1062-2 SCOPE of ACCREDITATION of the Calibration Laboratory MED CONTROL SERVICES O.E. PAPANIKOLAS ANTONIS & CO O.E.

| Calibration item / Parameters | Range of measurement | Expanded Measurement Uncertainty (k=2)* | Remarks |
| --- | --- | --- | --- |
| Volume Measurements |
| Liquid volume / Fixed storage tanks including alcoholic beverages tanks | 0.5 m3 to 10 m3 | 0.13 % of nominal volume | Volumetric method using flow meter according to: ISO 4269:2001 Calibration medium: Water Liquid hydrocarbons (gasoline, diesel oil, bio-diesel, JET A1) – for fuel tanks only Calibration is performed on site. |
|  | 10 m3 to 200 m3 | 0.08 % of nominal volume |  |
| Liquid volume / Road tankers | 0.5 m3 to 10 m3 | 0.13 % of nominal volume | Volumetric method using flow meter according to: ISO 4269:2001 OIML R 80-2:2017 – Annex Β Calibration medium: Water Liquid hydrocarbons (gasoline, diesel oil, bio-diesel, JET A1) Calibration is performed on site. |
|  | 10 m3 to 80 m3 | 0.08 % of nominal volume |  |
| Liquid Volume / Horizontal cylindrical tanks including alcoholic beverages tanks | 5 m3 to 400 m3 | 0.03 % of nominal volume | Geometric method using strapping tape according to: ISO 12917-1:2017 ISO 7507-1:2003 (other measurements) Calibration is performed on site. |
| Liquid volume / Vertical cylindrical tanks including alcoholic beverages tanks | 15 m3 to 200000 m3 maximum tank diameter: 100 m | Volume (m3) Uncertainty (%) 15 0.28 30 0.17 200 0.12 2000 0.12 ≥10000 0.11 of nominal volume | Geometric method using strapping tape according to: ISO 7507-1:2003 Calibration is performed on site. |
|  | above 250 m3 minimum tank diameter: 8 m | Volume (m3) Uncertainty (%) 250 0.19 500 0.13 2000 0.09 10000 0.07 ( 30000 0.06 of nominal volume | Geometric method using total station according to: ISO 7507-3:2006 ISO 7507-1:2003 (other measurements) Calibration is performed on site. |
|  | above 200 m3 minimum tank diameter: 5 m | Volume (m3) Uncertainty (%) 200 0.16 2000 0.09 10000 0.07 ( 40000 0.06 of nominal volume | Geometric method using total station according to: ISO 7507-4:2010 ISO 7507-1:2003 (other measurements) Calibration is performed on site. |

* Where the expanded uncertainty (with 95 % coverage) is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

The Calibration Measurement Capability (CMC) includes the measured quantity, the measurement range and the measurement uncertainty, expressing the minimum measurement uncertainty which can be achieved in a calibration.

Permanent laboratory premises address: Schina 37, Megara 19100, Greece

Approved Signatories:  N. Papanikolas, S. Papanikolas

This Scope of Accreditation replaces the previous one dated 16.03.2021.

The Accreditation Certificate No. 1062-2, to ELOT EN ISO/IEC 17025:2017, is valid until 29.09.2024.

Athens, 18.10.2023

Christos Nestoras

CEO of ESYD