Hellenic Accreditation System

| Annex F2/19 to the Certificate No. 117-7 SCOPE of ACCREDITATION of the Calibration Laboratory of the GREEK ATOMIC energy COMMISSION (ΕΕΑΕ) |
| --- |
| Measurand / Calibration item | Range of measurement | Expanded measurement uncertainty (k=2)* | Remarks |
| Radiation measurements |
| Ionization chambers and electrometers used in Radiotherapy in terms of Nk and ND,w | Energy: Co60 Kair rate : 400 mGy/min (Apr. 2012) Dose rate in water: 400 mGy/min (Apr. 2012) | Nk: 0,8 % ND,w: 0,9 % | IEC 60731:2011 IAEA TRS 469: 2009 IAEA TRS 277: 1987 IAEA TRS 381:1997 IAEA TRS 398:2000 |
| Instruments used in Radiation Protection for the detection and measurement of gamma and X radiation: Survey meters Geiger Scintillation detectors Analog detectors Ionization chambers | Energies: Cs137, x-ray (N40-N200) & Co60 Air kerma rate, K: 0,001 to 10 mGy/h (Cs137) 0,1 to 15 mGy/h (x-ray) 0,001 to 45000 mGy/h (Co60) H*(10) rate: 0,001 to 10 mSv/h (Cs137) 0,1 to 15 mSv/h (x-ray) 0,001 to 45000 mSv/h (Co60) | Nk: 2,4 % NΗ*(10) : 4,6 % | ISO 4037-1:2019 ISO 4037-2:2019 ISO 4037-3:2019 ISO 4037-4:2019 ΕΛΟΤ ΕΝ 61526:2013 ΕΝ 60846-1:2014 IEC 60846-2:2015 ΙΑΕΑ TRS 16:2000 ICRU 39:1985 ICRU 43:1988 ICRU 47:1992 ICRU 51:1993 |
| Measurand / Calibration item | Range of measurement | Expanded measurement uncertainty (k=2)* | Remarks |
| Dosimeters used in Diagnostic Radiology: Ionization chambers Solid state detectors Electrometers | Energies : x-ray RQR, RQR-M, RQT according to ISO/IEC 61267 qualities | Nk: 2,2 % NPKA: 2,5 % NPKL: 3,0 % | ΕΛΟΤ ΕΝ 61674:2014 IEC 61267: 2005 IAEA TRS 457: 2007 |
| Non invasive instruments used in diagnostic radiology for the measurement of the radiological parameters: KVp-meters | High Voltage: 20 kV to 35 kV (mammographic applications) 50 kV to 150 kV (diagnostic applications) | 2,0 % | IEC 61676:2002 + A1:2009 IAEA TRS 457: 2007 |
| Personal dosimetric instruments: Electronic dosimeters Pen type dosimeters TLD badges Film badges | Energies : Cs137, x-ray N40-N200 (ISO Narrow) & Co60 Equivalent dose Hp(10) & Hp(0.07): 1μSv to 10 μSv | N Ηp(10): 4,6 % N Ηp(0.07): 4,6 % | ISO 4037-1:2019 ISO 4037-2:2019 ISO 4037-3:2019 ISO 4037-4:2019 ΕΛΟΤ ΕΝ 61526:2013 IEC 62387:2020 IAEA TRS 16:2000 ICRU 39:1985 ICRU 43:1988 ICRU 47:1992 ICRU 51:1993 |

* 	Where uncertainty is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

Site of assessment: Permanent laboratory premises, P. Gregoriou E΄ & Neapoleos, Ag. Paraskevi, Attiki, Greece.

Approved Signatories: A. Boziari, E. Karabetsos.

This Scope of Accreditation replaces the previous one dated January 17th, 2023.

The Accreditation Certificate No. 117-7, to ELOT EN ISO/IEC 17025: 2017, is valid until 21.01.2028.

Athens, July 21st, 2023

Christos Nestoras

CEO of ESYD