Hellenic Accreditation System

Annex F1/20 to the Certificate No. 57-7 SCOPE of ACCREDITATION of the Testing laboratory "Dimitris I. Oikonomidis, Analytical Laboratory of Rhodes" OIKONOMIDIS R.T.I. Ltd.

| Tested materials / products | Types of test / Properties to be measured | Applied Standards / Techniques to be used |
| --- | --- | --- |
| Chemical Tests |
| 1. Surface, household, swimming pools and drinking water | 1. Determination of conductivity | APHA* 2510 B, 23rd Edition 2017 |
|  | 2. Determination of pH | APHA* 4500-H B, 23rd Edition 2017 |
|  | 3. Determination of total hardness | APHA* 2340 C, 23rd Edition 2017 |
|  | 4. Determination of calcium | APHA* 3500-Ca B, 23rd Edition 2017 |
| 2. Surface, swimming pools, household and drinking water | Determination of alkalinity | APHA* 2320 B, 23rd Edition 2017 |
| 3. Surface, swimming pools, household and drinking water. Soil | Determination of chlorides | APHA* 4500-Cl B, 23rd Edition 2017 |
| 4. Wastes | 1. Determination of BOD** | Modified method based on APHA* 5210 B, 23rd Edition 2017 |
|  | 2. Determination of COD*** | Modified method based on APHA* 5220 B, 23rd Edition 2017 |
|  | 3. Determination of COD*** | Method HACH LCK 314 |
|  | 4. Determination of total suspended solids (TSS) | Modified method based on APHA* 2540 D, 23rd Edition 2017 |
| 5. Pool water | Determination of cyanuric acid **** | Turbidimetric method, HACH 8139 modified |
| Microbiological Tests |
| 1. Surface, swimming pool and drinking water | Enumeration of total viable count (22 and 36 oC) | ISO 6222:1999 |
| 2. Surface, swimming pool, drinking and cooling equipment water | Detection and enumeration of Legionella spp. | ISO 11731: 2017 |
| 3. Surface, swimming pool, Sea Water, and drinking water, wastewater | Enumeration of enterococci | ISO 7899-2:2000 |
| 4. Surface, wastewater, swimming pool, Sea Water, and drinking water | Enumeration of coliforms and E. coli | ISO 9308-1:2014/Amd 1:2016 |
| 5. Drinking and swimming pool water | Εnumeration of Pseudomonas aeruginosa | ISO 16266:2006 |
| 6. Milk | 1. Enumeration of total viable count (30oC) | ISO 4833-1:2013 |
|  | 2. Enumeration of coliforms | ISO 4832:2006 |
| 7. Foods and environmental samples | Detection of Salmonella spp. | VIDAS® Salmonella (VIDAS SLM) bioMérieux, Validation Certificate AFNOR BIO 12/10-09/02 |
| 8. Foodstuff and animal feed | Enumeration of E. coli | ISO 16649-2:2001 |

*  American Public Health Association, American Water Works Association, Water Environment Federation, “Standard Methods for the Examination of Water and Wastewater”, 23rd Edition 2017

** BOD:  biochemical oxygen demand

*** COD: chemical oxygen demand

**** at concentration level > 15 mg/L

Site of assessment: Laboratory permanent premises, 1 Vironos Street, 851 32 Rhodes, Greece

Approved signatories: D. Oikonomidis, A. Sarika-Oikonomidou, Ε. Oikonomidou

This Scope of Accreditation replaces the previous one, dated 06.06.2022.

The Accreditation Certificate No. 57-7, according to ELOT EN ISO/IEC 17025:2017, is valid until 10.12.2026.

Athens, 1st of February 2023

Christos Nestoras

CEO of ESYD