Hellenic Accreditation System

Annex F2/8 to the Certificate No. 891-4 SCOPE of ACCREDITATION of the Calibration Laboratory of METRICON S.A.

| Measurand / Calibration item | Range of measurement | Calibration & Measurement Capability (k=2)* | Remarks |
| --- | --- | --- | --- |
| Mass Measurements |
| Mass / Standard weights |  |  | Capability to calibrate standard weights up to (including): OIML Class, R111-1:2004 |
|  | 1 kg | 11 mg | Μ1 |
|  | 2 kg | 11 mg | M1 |
|  | 5 kg | 14 mg | F2 |
|  | 10 kg | 60 mg | M1 |
|  | 20 kg | 38 mg | F2 |
|  | 50 kg | 1,3 g | M1-2 |
|  | 100 kg | 2,4 g | M1-2 |
|  | 200 kg | 2,8 g | M1 |
|  | 500 kg | 19 g | M2 |
|  | 1000 kg | 30 g | M1-2 |
| Mass / Non-automatic weighing instruments | 1 kg | 83 mg | According to guide EURAMET/cg-18/v.04 Available standard weights OIML / Max load: Class M1: 1 kg - 20 kg / 1002 kg Class M1-2: 50kg - 100 kg / 200 kg Class M2: 500 kg - 1000 kg / 19000 kg Calibration is performed on-site. |
|  | 2 kg | 0,17 g |  |
|  | 5 kg | 0,4 g |  |
|  | 10 kg | 0,8 g |  |
|  | 20 - 400 kg | 1,7 x N (g) N: number of standard weights of nominal mass 20 kg (N=1…20) |  |
|  | 500 kg | 130 g |  |
|  | 1000 kg | 270 g |  |
|  | 1000 - 19000 kg | m x 2.7 x 10-4 m: mass value in kg |  |
|  | 19000 kg d=10 kg d=20 kg | 10 kg 17 kg | According to guide EURAMET/cg-18/v.04 using substitution loads of known density provided by the client Calibration is performed on-site |
|  | 38000 kg d=10 kg d=20 kg | 20 kg 33 kg |  |
|  | 57000 kg d=10 kg d=20 kg | 31 kg 55 kg |  |
| Volume Measurements |
| Liquid Volume / Metallic tanks | 0,5 – 100 m3 | 0,11% of nominal tank volume | Gravimetric method according to guide EURAMET/cg-19/v.3 (2018) Calibration medium: Tap water Calibration is performed on-site |
| Liquid Volume / Road tankers | 0,5 – 45 m3 | 0,24% of nominal tank volume | Gravimetric method according to guides: EURAMET/cg-19/v.3 (2018) OIML R80-2:2017, Annex B Calibration medium: Tap water Calibration is performed on-site |

*Where uncertainty is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, is relative.

Site of assessment: Permanent laboratory premises, Athinon str 65, 26 504 Rio, Patras, Greece

Approved Signatories: A. Lampou, G. Tsolkas

This Scope of Accreditation replaces the previous one dated 5.10.2021.

The Accreditation Certificate No. 891-4, to ELOT EN ISO/IEC 17025:2017, is valid until 10.10.2025.

Athens, 19.04.2022

Christos Nestoras

CEO of ESYD