Hellenic Accreditation System

Annex F2/7 to the Certificate No. 1094-3 SCOPE of ACCREDITATION of the Calibration Laboratory of pantelidis s.a. Distinctive title: PANMETRO

| Measurand / Calibration item | Range of measurement | Calibration & Measurement Capability (k=2)* | Remarks |
| --- | --- | --- | --- |
| Mass Measurements |
| Mass / Standard weights | 10 kg | 0,16 g | Calibration of standard weights according to OIML R 111-1:2004 (Ε). Standard weight calbration capability up to (and including): OIML Class M1 |
|  | 20 kg | 0,3 g |  |
|  | 50 kg | 2,5 g | Calibration of standard weights according to PTB Bericht PTB-MA-80e (2007). Standard weight calbration capability up to (and including): OIML Class M2 |
|  | 100 kg | 5 g |  |
|  | 500 kg | 25 g | Calibration of standard weights according to OIML R 111-1:2004 (Ε). Standard weight calbration capability up to (and including): OIML Class M2 |
|  | 1000 kg | 50 g |  |
| Mass / Non-automatic weighing instruments | 1 mg | 0,14 mg | Calibration according to guide EURAMET /cg-18/v.04 (11/2015). Use of standards of OIML R 111 class: M1 in range 1 mg … 20 kg. Max grouped load: 628,8 kg M2 in range 50 kg …1 t. Max grouped load: 20,3 t Calibration is performed on-site. |
|  | 2mg | 0,24 mg |  |
|  | 5 mg | 0,24 mg |  |
|  | 10 mg | 0,30 mg |  |
|  | 20mg | 0,37 mg |  |
|  | 50 mg | 0,49 mg |  |
|  | 100 mg | 0,61 mg |  |
|  | 200 mg | 0,73 mg |  |
|  | 500 mg | 0,97 mg |  |
|  | 1 g | 1,2 mg |  |
|  | 2 g | 1,5 mg |  |
|  | 5 g | 2,0 mg |  |
|  | 10 g | 2,4 mg |  |
|  | 20 g | 3,0 mg |  |
|  | 50 g | 3,7 mg |  |
|  | 0,1 kg … 5 kg | 6,1 . 10-5 |  |
|  | 10 kg… 600 kg | 6,1 . 10-5 |  |
|  | 600 kg … 20 t | 2,0. 10-4 |  |
|  | 0,5 t … 3 t | kg | Calibration according to guide EURAMET /cg-18/v.04 (11/2015), with use of substitution loads. Where: Ι, Max load indication in kg, d, the instrument's readability in kg Ν the calibration step ( number of substition loads + 1) Calibration is performed on-site. |
|  | 3 t … 60 t | kg |  |

* Where uncertainty is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

Site of assessment: Permanent Laboratory premises, 12 klm O.N.R. Thessaloniki - Kilkis, 54500, Thessaloniki.

Approved Signatories: Angelos Tsiatsis, Georgios Pantelidis.

- This scope of Accreditation replaces the previous one dated 11.08.2021.

- The Accreditation Certificate No. 1094-3, to ELOT EN ISO/IEC 17025:2017, is valid until 11.06.2025.

Athens, 13.01.2023

Christos Nestoras

CEO of ESYD