Hellenic Accreditation System

Annex F2/11 to the Certificate No. 922-4 SCOPE of ACCREDITATION of the Calibration Laboratory of DOMIKI PROODOS S.A.

| Measurand / Calibration item | Range of measurement | Calibration & Measurement Capability (k=2)* | Remarks |
| --- | --- | --- | --- |
| Volume measurements |
| Fixed storage tanks | 0,5 m3 to 50 m3 | 0,06 % of nominal tank volume | Volumetric method using volumetric vessel according to: EURAMET cg-21, v.2.1: 2021 Calibration medium: Tap water. Calibration is performed on site. |
| Fixed storage tanks, including tanks of alcoholic beverages | 0,2 m3 to 750 m3 | 0,08 % of nominal tank volume | Volumetric method using flow meter according to: ISO 4269:2001 Calibration medium: Tap water or other liquid with similar volatility and viscosity or suitable petroleum product. Calibration is performed on site. |
| Road tankers | 0,2 m3 to 80 m3 | 0,08 % of nominal tank volume | Volumetric method using flow meter according to: - ISO 4269:2001 - OIML R 80-2: 2017 - Annex B Calibration medium: Tap water or other suitable petroleum product. Calibration is performed on site. |
| Steel volumetric vessels of types “to deliver” | 0,02 m3 to 2 m3 | 0,07 % | Volumetric method using volumetric vessels according to: EURAMET cg-21, v.2.1: 2021 except neck calibration Calibration medium: Potable water. |
| Vertical cylindrical tanks, including tanks of alcoholic beverages | 0,75 m3 to 2700 m3 Max tank diameter 15 m | Diame- ter Height 1 m 3 m 5 m > 7,5 m 1 m 0,59 % 0,36 % 0,34 % 0,33 % 2 m 0,53 % 0,25 % 0,21 % 0,20 % > 3 m 0,52 % 0,22 % 0,18 % 0,16 % on nominal tank volume | Calibration according to: ISO 7507-1:2003 Measurement of bottom volume according to: ISO 4269:2001 Calibration is performed on-site. |

* Where uncertainty is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, is relative

Site of assessment: Permanent laboratory premises, Petras str 3, 12241, Aigaleo, Attiki, Greece.

Approved Signatory: Nikolaos Ventouris, Christos Boubousis.

This Scope of Accreditation replaces the previous one dated 3.03.2023.

The Accreditation Certificate No. 922-4, to ELOT EN ISO/IEC 17025: 2017, is valid until 14.09.2027.

Athens, 16.03.2023

Christos Nestoras

CEO of ESYD