Hellenic Accreditation System

Annex F2/13 to the Certificate No. 738-6 SCOPE of ACCREDITATION of the Calibrations Laboratory of METRON S.A.

| Calibration item / Parameters | Range of measurement | Expanded measurement uncertainty (k=2)* | Remarks |
| --- | --- | --- | --- |
| Volume measurements |
| Steel volumetric vessels of type “to contain (wet)” and “to deliver” | [10 to 100) L | 0,06 % | Using volumetric vessels according to standards: API MPMS CHAPTER 4: Proving Systems SECTION 4: Tank provers (1998) SECTION 7: Field Standard Test Measures (2009) Calibration medium: potable water. Calibration can also be performed on site. |
|  | [100 to 500) L | 0,04 % |  |
|  | [500 to 5000) L | 0,05 % |  |
|  | [5000 to 10000] L | 0,06 % |  |
| Positive displacement meters | [0,5 to 120] m3/h | 0,08 % | Using volumetric vessels according to standards: API MPMS CHAPTER 4: Proving Systems SECTION 5: Master Meter Provers (2016) SECTION 8: Operation of Proving Systems (2021) Calibration medium: liquid refined products and lubricant oils. according to API MPMS. Calibration can also be performed on site. |
| Coriolis meters |  | 0,1 % | Using volumetric vessels according to standards: API MPMS CHAPTER 4: Proving Systems SECTION 5: Master Meter Provers (2016) SECTION 8: Operation of Proving Systems (2021) CHAPTER 5: Metering SECTION 6: Measurement of Liquid Hydrocarbons by Coriolis Meters (2021) Calibration medium: liquid refined products and lubricant oils. according to API MPMS. Calibration can also be performed on site. |
| Positive displacement meters | [0,5 to 120] m3/h | 0,11 % | Using positive displacement master meter according to standards: API MPMS CHAPTER 4: Proving Systems SECTION 5: Master Meter Provers (2016) SECTION 8: Operation of Proving Systems (2021) Calibration medium: liquid refined products and lubricant oils according to API MPMS. Calibration can also be performed on site. |
|  |  | 0,12 % | Using Coriolis master meter according to standards: API MPMS CHAPTER 4: Proving Systems SECTION 5: Master Meter Provers (2016) SECTION 8: Operation of Proving Systems (2013) CHAPTER 5: Metering SECTION 6: Measurement of Liquid Hydrocarbons by Coriolis Meters (2021) Calibration medium: liquid refined products and lubricant oils according to API MPMS. Calibration can also be performed on site. |
| Coriolis meters | [0,5 to 120] m3/h | 0,13 % | Using positive displacement master meter according to standards: API MPMS CHAPTER 4: Proving Systems SECTION 5: Master Meter Provers (2016) SECTION 8: Operation οf Proving Systems (2021) CHAPTER 5: Metering SECTION 6: Measurement of Liquid Hydrocarbons by Coriolis Meters (2021) Calibration medium: liquid refined products and lubricant oils according to API MPMS. Calibration can also be performed on site. |
|  |  | 0,13 % | Using Coriolis master meter according to standards: API MPMS CHAPTER 4: Proving Systems SECTION 5: Master Meter Provers (2016) SECTION 8: Operation of Proving Systems (2013) CHAPTER 5: Metering SECTION 6: Measurement of Liquid Hydrocarbons by Coriolis Meters (2021) Calibration medium: liquid refined products and lubricant oils according to API MPMS. Calibration can also be performed on site. |
| Positive Displacement meters | [0,5 to 120] m3/h | 0,10 % | Using volumetric vessels according to standard: ISO 4269:2001 Calibration medium: potable water. Calibration can also be performed on site. |
| Coriolis meters | [ 0,5 to 120] m3/h | 0,10 % | Using volumetric vessels according to standards: ISO 4269:2001 API MPMS CHAPTER 5: Metering SECTION 6: Measurement of Liquid Hydrocarbons by Coriolis Meters (2021) Calibration medium: potable water. Calibration can also be performed on site. |
| Pipe provers | [0.02 to 10] m3 (Round trip) | 0,06 % | Using volumetric vessels according to standards: API MPMS CHAPTER 4: Proving Systems SECTION 2: Displacement Provers (2003 with Addendum 1 dated February 2015) SECTION 5: Master Meter Provers (2016) SECTION 8: Operation of Proving Systems (2021) Calibration medium: potable water. Calibration is performed on-site. |
| Temperature Measurements |
| Resistance sensors with direct, analog or digital reading | [-20 0C to 100 0C] | 0,05 0C | DKD-R 5-1 (09/2018) Calibration can also be performed on-site. |
|  | (100 0C to 120 0C] | 0,08 0C |  |
| Resistance sensors with indirect reading in ohm | [-20 0C to 100 0C] | 0,05 0C |  |
|  | (100 0C to 120 0C] | 0,08 0C |  |
| Resistance sensors with indirect reading in mA | [-20 0C to 100 0C] | 0,07 0C |  |
|  | (100 0C to 120 0C] | 0,09 0C |  |

* Where uncertainty is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, is relative.

Site of assessment: Permanent laboratory premises, 45 D. Rigou Str. 19018 Magoula, Greece.

Approved Signatories: S. Valsamos, A. Boutos.

This Scope of Accreditation replaces the previous one dated 27.04.2023.

The Accreditation Certificate No. 738-6, to ELOT EN ISO/IEC 17025: 2017, is valid until 26.05.2028.

Athens, August 21st, 2023

Christos Nestoras

CEO of ESYD