Hellenic Accreditation System

Annex F1/6 to the Certificate No. 635-5 SCOPE of ACCREDITATION of the Wastewater Treatment Plant Laboratory of Water Sewage Municipal Agency of the Greater Volos Area

| Materials / Tested products | Type of test / Measured properties | Applied standards / Techniques used |
| --- | --- | --- |
| Chemical Testing |
| 1. Wastewater and water | 1. Determination of total suspended solids (TSS) | APHA* 2540D |
|  | 2. Determination of chemical oxygen demand (COD) | In house method based on APHA* 5220D. Closed Reflux, Colorimetric Method |
|  | 3. Determination of Ammonium (NH4+) | Method HACH LCK 304, 305 |
|  | 4. Determination of Total Phosphorous (P-PO4) | Method HACH LCK 349 |
| 2. Non disinfected urban Wastewater | Determination of biochemical oxygen demand (BOD5) | In house method based on APHA* 5210D. Biochemical Oxygen Demand – Respirometric Method |

*Standard Methods for the Examination of Water & Wastewater, APHA AWWA WEF, 23rd Edition 2017.

Site of assessment: Permanent laboratory premises, Wastewater Treatment Plant, DEYAMV,

Bourboulithra, Volos 383 34, Greece

Approved Signatories: Sofia Tresintsi, Vaios Zebeoglou

This Scope of Accreditation replaces the previous one, dated 10.09.2021.

The Accreditation Certificate No 635-5, according to ELOT EN ISO/IEC 17025:2017, is valid until 22.11.2025.

Athens, 6th of March 2023

Christos Nestoras

CEO of ESYD