Hellenic Accreditation System

Annex F1/4 to the Certificate No. 1169-2 SCOPE of ACCREDITATION of the Department of Laboratories, Directorate of Technical Control, of the North Aegean Region-Regional Unit of Chios

| Materials / Products to be tested | Types of test / Properties to be measured. | Applied methods / Techniques to be used |
| --- | --- | --- |
| Physical & Chemical Testing |
| Hardened Concrete | Testing hardened concrete Part 2: Making and curing of test specimens (15cm x 15cm x 15cm) for strength tests | ΕLΟΤ ΕΝ 12390-2 Ε3: 2019 |
| Freshly mixed Concrete | Testing fresh concrete Part 2: Slump test | ΕLΟΤ ΕΝ 12350-2 E3: 2019 |
| Aggregates | 1.Tests for geometrical properties of aggregates Part 1: Determination of particle distribution – Sieving method | ELOT ΕΝ 933-1 E2: 2012 |
|  | 2.Tests for geometrical properties of aggregates Part 8: Assessment of fines – Sand equivalent test | ELOT ΕΝ 933-8: 2012 +A1:2015 |
|  | 3.Tests for geometrical properties of aggregates Part 9: Assessment of fines – Methylene blue test | ELOT ΕΝ 933-9: 2009 A1:2013 |
| Αggregates of bituminous mixtures | Bituminous mixtures - Test methods - Part 2: Determination of particle size distribution | ΕLΟΤ EN 12697-2+A1:2019 |

| Materials / Products to be tested | Types of test / Properties to be measured | Applied methods / Techniques to be used |
| --- | --- | --- |
| Physical & Chemical Testing |
| Bituminous mixtures | 1.Bituminous mixtures - Test methods - Part 39: Binder content by ignition | ΕLΟΤ ΕΝ 12697-39 E2 :2012 |
|  | 2.Bituminous mixtures - Test methods for hot mix asphalt - Part 6: Determination of bulk density of bituminous specimens | ΕLΟΤ ΕΝ 12697-6 :2012 |
| Soils | Density of soils in place – Determination by the sand & cone method | Technical Standard of HMEPPPW Ε 106-86, §2 |
| Mechanical Testing |
| Soils | Test for moisture – density relations of soils using 4,54 kg rammer and 457 mm drop (Proctor modified method) | Technical Standard of HMEPPPW Ε 105-86, §11 |
| Hardened concrete | 1.Testing hardened concrete - Part 3: Compressive strength of test specimens | ΕLΟΤ ΕΝ 12390-3 E3: 2019 |
|  | 2.Testing concrete in structures - Part 1: Cored specimens - Taking, examining and testing in compression | ΕLΟΤ ΕΝ 12504-1 E3 : 2020 |

Site of assessment: Permanent Premises Samou 1 Chios

Approved signatories: Kartalis Christos, Stathopoulos Theodosis

This Scope of Accreditation replaces the previous one dated 09.06.2023.

The Accreditation Certificate No.1169-2 to ELOT EN ISO/IEC 17025: 2017, is extended until 10.06.2024.

Athens, 08.12.2023

Christos Nestoras

CEO of ESYD