Hellenic Accreditation System

Annex F2/2 to the Certificate No. 1258

SCOPE of ACCREDITATION

of the

Calibration Laboratory

of

KAISIS OIL GROUP S.A. (NICK TRANS S.A.)

| Measurand / Calibration item | Range of measurement | Calibration & Measurement Capability (k=2)* | Remarks |
| --- | --- | --- | --- |
| Volume measurements |
| Liquid volume / Fixed metallic tanks | 1 m3 – 200 m3 | 0,12 % of nominal tank volume | Volumetric method through the use of volumetric standard Standards followed: EURAMET cg-21 Version 2.1 (09/2021) Calibration medium: Tap water The calibration can be performed on site. |
| Liquid volume / Road metallic tanks | 0,5 m3 – 40 m3 | 0,12 % of nominal tank volume | Volumetric method through the use of volumetric standard Calibration medium: Tap water Standards followed: EURAMET cg-21 Version 2.1 (09/2021) OIML R80-2: 2017, Annex B The calibration can also be performed on site |

Site of assessment: Permanent premises, Proektasi Makrigianni, Evosmos, Thessaloniki, Greece.

Approved Signatories: Dimitrios Polychronakos, Christos Zikidis.

This Scope of Accreditation replaces the previous one dated 08.06.2021.

The Accreditation Certificate No. 1258, to ELOT EN ISO/IEC 17025:2017, is valid until 07.06.2025.

Athens, 17.06.2022

Christos Nestoras

CEO of ESYD