Hellenic Accreditation System

Annex F2/2 to the Certificate No. 1260

SCOPE of ACCREDITATION the Calibration Laboratory of the Section Laboratories and Radios / Network Department of HEDNO - HELLENIC ELECTRICITY DISTRIBUTION NETWORK OPERATOR

| Measurand / calibration item | Range of measurement | Calibration & Measurement Capability (k=2)* | Applied standards |
| --- | --- | --- | --- |
| Electrical Measurements |
| Power meters / Active power | Voltage: up to 400 V Current: [5 mA - 50 mA] (50 mA - 10 A) [10 A - 120 A] cosφ = 1 / 0,5 1 ή 3 Phase - 50 Hz cosφ = 1 / 0,5i / 0,8c 2 Phase / 3 wire - 50 Hz | 0,016% 0,011% 0,013% | EN 62052-11: 2020 EN 62053-21: 2020 EN 62053-22: 2020 |
| Power meters / Reactive power | Voltage: up to 400 V Current: 5mA - 120A sinφ = 1 / 0,5 1 ή 3 Phase - 50 Hz | 0,017% | EN 62052-11: 2020 EN 62053-23: 2020 |
| Current transformers / - Ratio error - Phase displacement | Primary: 0 - 1000 A Secondary: 1 - 5 A Excitation: 200%, 120%, 100%, 80%, 20%, 5%, 1% Frequency: 50 Hz | 0,03% 1,5 min of arc | IEC 61869-1: 2007 IEC 61869-2: 2012 |
| Voltage Transformers / - Ratio error - Phase Displacement | Primary: 15 - 22 kV Secondary: 100 V, 110 V, 110/√3 V, 100/√3 V Excitation: 120%, 100%, 80% Frequency: 50 Hz | 0,03% 1,5 min of arc | IEC 61869-1: 2007 IEC 61869-3: 2011 |

* Where uncertainty is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

Site of assessment: 70 Agias Annis str, 122 41 Egaleo, Attiki, Greece

Approved Signatories: Panagiotis Chlampeas, Antonios Xenopoulos, Konstantinos Anastasakis

This scope of Accreditation replaces the previous one dated 25.06.2021.

The Accreditation Certificate No. 1260, to ELOT EN ISO 17025:2017, is valid until 24.06.2025.

Athens, 23.03.2023

Christos Nestoras

CEO of ESYD