Hellenic Accreditation System

Annex F1/11 to the Certificate No. 919-4 SCOPE of ACCREDITATION of the Laboratory of Hygiene and Epidemiology of School of Medicine, University of Ioannina

| Tested materials and products | Types of test / Properties to be measured | Applied standards / Techniques to be used |
| --- | --- | --- |
| Microbiological Tests |
| 1. Potable Water, Surface Water, swimming pool water and sea water | 1. Εnumeration of coliforms and Escherichia coli | ΙSO 9308-1:2014 Amd 1:2016 |
|  | 2. Detection and enumeration of Pseudomonas aeruginosa | ISO 16266:2006 |
|  | 3. Detection and enumeration of intestinal enterococci | ISO 7899-2:2000 |
|  | 4. Enumeration of culturable micro-organisms at 22(2 οC and at 36(2 οC | ISO 6222:1999 |
| 2. Potable Water, Surface Water and Swimming Pool water | Enumeration of Clostridium perfringens (including spores) | ISO 14189:2013 |
| 3. Water with low concentration of interfering microorganisms (Matrix A) | Enumeration of Legionella spp. | ISO 11731:2017 Procedure 5,7, Medium A & C-GVPC Procedure 8,9,10 Medium A & C-GVPC |
| 4. Water with a high concentration of interfering microorganisms (Matrix B) | Enumeration of Legionella spp. | ISO 11731:2017 Procedure 1,2,3 Medium C-GVPC Procedure 8,9,10 Medium C-GVPC Procedure 11,12,13 Medium C-GVPC |
| 5. Treated wastewater from treatment plant 5. Treated wastewater from treatment plant (continued) | 1. Enumeration of coliforms and Escherichia coli | ΙSO 9308-1:2014 Amd 1:2016 |
|  | 2. Detection and enumeration of intestinal enterococci | ISO 7899-2:2000 |
| Chemical Tests |
| 1. Water and Wastewater | 1. Determination of pH | APHA 4500-H+ B |
|  | 2. Determination of Conductivity | ASTM D1125-95 |
|  | 3. Determination of Turbidity | APHA 2130 B |
|  | 4. Determination of Total Dissolved Solids (T.D.S.) | APHA 2540 C |
|  | 5. Determination of Chemical oxygen demand (COD) | APHA 5220 D |
|  | 6. Determination of Biochemical oxygen demand (BOD) | APHA 5210 B |
|  | 7. Determination of Total nitrogen | LCK138, HACH (based on EN ISO 11905-1 and ISO23697-1) |
|  | 8. Determination of Total phosphorus | APHA 4500-P E |
| 2. Potable Water, Surface Water, swimming pool water 2. Potable Water, Surface Water, swimming pool water (continued) | 1. Determination of nitrate ions | APHA 4500-NO3- B |
|  | 2. Determination of nitrite ions | APHA 4500-NO2- B |
|  | 3. Determination of Ammonium ions | In house method, salicylate hypochlorite method (Method Code: US3432395A) |
|  | 4. Determination of Residual chlorine | APHA 4500-Cl G |
|  | 5. Determination of Iron | LCK521, HACH (based on ISO 6332-1988 standard and DIN 38406 E1-1 standard) |
|  | 6. Determination of Sulphate ions | SulfaVer 4, HACH (based on USEPA 375.4 and APHA 4500-SO4-2 Ε) |
|  | 7. Determination of Copper | LCK329, HACH (Bathocuproine disulphonic acid method) |
|  | 8. Determination of Potassium | LCK228, HACH (Kallignost method) |
|  | 9. Determination of Cadmium | In-house method based on APHA 3113 B |
|  | 10. Determination of Nickel | In-house method based on APHA 3113 B |
|  | 11. Determination of Chromium | In-house method based on APHA 3113 B |

Site of assessment: Permanent Laboratory premises, School of Medicine, University Campus of Ioannina

Approved signatories: K. Tsilidis

This scope of Accreditation replaces the previous one, dated 06.03.2023.

The Accreditation Certificate No. 919-4, according to ELOT EN ISO/IEC 17025:2017, is valid until 19.05.2027.

Athens, 29th of March 2024

Christos Nestoras

CEO of ESYD