Hellenic Accreditation System

Annex F1/11 to the Certificate No. 757-4

SCOPE of ACCREDITATION

of the

Testing Laboratory

of the

Water Supply & Sewerage Company of Municipality of Larissa

| Materials / Products tested | Types of test / Properties measured | Applied methods / Techniques used |
| --- | --- | --- |
| Chemical Tests |
| 1. Drinkable water, underground water, surface water, and pool water | 1. Determination of pH | ΕLOT 658:1983 |
|  | 2. Determination of conductivity | Based on ΕLΟΤ ΕΝ 27888:1993 |
| 2. Drinkable water, underground water, surface water | 1. Determination of Cl-`, NO3-, SO42- | ISO 10304-1:2007 |
|  | 2. Determination of Mn | HACH LCK 532 |
|  | 3. Determination of Fe | HACH LCK 521 |
|  | 4. Determination of NH4+ | HACH LCK 304 |
|  | 5. Determination of Cr | Based on ELOT EN ISO 15586:2003 |
|  | 6. Determination of As | Based on ISO 17378-2:2014 |
|  | 7. Determination of Cu | ELOT EN ISO 8288:1986 |
|  | 8. Determination of Ni | Based on ISO 15586:2003 |
|  | 9. Determination of Pb | Based on ISO 15586:2003 |
|  | 10. Determination of Cd | Based on ISO 15586:2003 |
|  | 11. Determination of Turbidity | ΕLΟΤ ΕΝ ISO 7027-1:2016 |
|  | 12. Determination of Color | Based on APHA 2120 *C |
| 3. Drinkable water, underground water | Determination of BrO3- | ISO 11206:2011 |
| 4. Drinkable water, underground water and pool water | Determination of chlorine residual | APHA4500-Cl. *G. |
| Microbiological Tests |
| 1. Drinkable, underground, surface and pool water | 1. Enumeration of Total Coliforms and E. Coli | ISO 9308-1:2014/ amd 1:2016 |
|  | 2. Detection and enumeration of intestinal enterococci | ISO 7899-2:2000 |
|  | 3. Detection and Enumeration of culturable micro-organisms at 22οC οC and 37οC | ISO 6222:1999 |
|  | 4. Detection and enumeration of Pseudomonas aeruginosa | ISO 16266:2006 |
| 2. Drinkable, underground and surface | Enumeration of Clostridium perfringens including spores | ISO 14189:2013 |
| Sensory Tests |
| Drinkable water, underground water | 1. Determination of Odor (ΤΟΝ) | In house method based on ELOT EN 1622:2006 and APHA 2150-2160C |
|  | 2. Determination of Taste (ΤFN) | In house method based on ELOT EN 1622:2006 and APHA 2160 C |
| Sampling |
| Drinkable, underground, surface and pool water | 1. Determination of Physicochemical Parameters | ELOT ΕΝ ISO 5667-3:2018 ISO 5667-5:2006 ISO 5667-6:2014 ISO 5667-11:2009 ISO 5667-14:2016 |
|  | 2. Determination of Microbiological Parameters | ISO 5667-3 :2018 ISO 5667-5:2006 ISO 5667-6:2014 ISO 5667-11:2009 ISO 5667-14:2016 ISO 19458:2006 |

*  American Public Health Association, American Water Works Association, Water Environment Federation,

“Standard Methods for the Examination of Water and Wastewater”, 23rd Edition, 2017

Site of assessement: Permanent laboratory premises - End of Tiherou, Larissa, Greece

Approved signatories: Ar. Papakonstantinou, D. Ntinouli

This scope of Accreditation replaces the previous one, dated 05.07.2023.

The Accreditation Certificate No. 757-4, according to ELOT EN ISO/IEC 17025:2017, has been extended until 13.07.2024.

Athens, 10th of January 2024

Christos Nestoras

CEO of ESYD