Hellenic Accreditation System S.A.

Annex F2/18 to the Certificate No. 388-5 SCOPE of ACCREDITATION of the Laboratory of CHIMIKI TECHNIKI MINESCHOS L.P. for the performance of calibrations

| Calibration item / Parameters | Range of measurement | Expanded measurement uncertainty (k=2) * | Remarks |
| --- | --- | --- | --- |
| Mass measurements |
| Non-automatic electronic weighing instruments |  |  | EURAMET cg-18 v.04:2015 Calibration is performed on site. Available standard weights OIML Class: |
|  | 1 mg 2 mg 5 mg 10 mg 20 mg 50 mg 100 mg 200 mg 500 mg 1 g 2 g 5 g 10 g 20 g 50 g 100 g | 3,8 x 10-3 1,9 x 10-3 7,5 x 10-4 3,8 x 10-4 1,9 x 10-4 1,0 x 10-4 6,3 x 10-5 3,8 x 10-5 2,0 x 10-5 1,3 x 10-5 7,5 x 10-6 4,0 x 10-6 2,5 x 10-6 1,6 x 10-6 0,8 x 10-6 0,6 x 10-6 | E1 |
|  | (100 g to 500 g] | 2,0 x 10-6 | E2 |
|  | (500 g to 4 kg] | 6,3 x 10-5 | M1 |
|  | (4 kg to 230 kg] | 2,0 x 10-4 | M2 |
| Standard weights |  |  | OIML R111-1:2004 Capability to calibrate standard weights up to OIML Class: |
|  | [1 mg to 10 mg] 20 mg 50 mg 100 mg 200 mg 500 mg 1 g 2 g 5 g 10 g 20 g 50 g 100 g 200 g | 2 μg 3 μg 3 μg 3 μg 4 μg 5 μg 5 μg 7 μg 8 μg 10 μg 13 μg 26 μg 31 μg 50 μg | E2 |
|  | 500 g | 1,5 mg | F2 |
|  | 1 kg 2 kg | 1,6 mg 2,1 mg | F1 |
|  | 5 kg 10 kg 20 kg | 0,22 g 0,26 g 0,34 g | M2 |
| Spectrophotometric measurements |
| Spectrophotometers / Absorption of visible and UV radiation in the range 200 nm to 900 nm | [0 to 0,5 AU] | 7,4 mAU** | ASTM E 275: 2008 (R2022) (baseline stability, photometric accuracy and precision) Calibration is also performed on site. |
|  | (0,5 AU to 1,0 AU] | 7,7 mAU |  |
|  | (1,0 AU to 2,2 AU] | 8,0 mAU |  |
| High-performance liquid chromatographs (HPLC) / Absorption of visible and UV radiation | [0 to 0,3 AU] | 10 mAU | ASTM E 1657: 1998 (2019) (noise & drift, photometric accuracy and precision) Calibration is also performed on site. |
|  | (0,3 AU to 1,0 AU] | 11 mAU |  |
| Plate readers / Absorption of visible radiation | [0 to 0,5 AU] | 10 mAU | ASTM E 275-08 (R2022) (photometric accuracy and precision) Calibration is also performed on site. |
|  | (0,5 AU to 1,0 AU] | 11 mAU |  |
|  | (1,0 AU 2,8 AU] | 14 mAU |  |
| Conductivity measurements |
| Conductivity detectors of ion chromatographs (IC) and high-performance liquid chromatographs (HPLC) | [0 to 15 μS/cm] | 0,2 μS/cm | ASTM E 1511: 1993 (2017) (noise & drift, conductivity accuracy and precision) Calibration is also performed on site. |
|  | (15 μS/cm to 150 μS/cm] | 1,0 μS/cm |  |
|  | (150 μS/cm to 1500 μS/cm] | 12 μS/cm |  |
| Electrical measurements |
| pH meters / DC voltage | -420 mV to +420 mV | 0,033 mV | Internal method ΜΔ-19.Γ using voltage simulator, based on guideline EURAMET cg-15:2015 The range of measurements corresponds to pH values 0 to 14. |
| Flow measurements |
| Liquid chromatography systems / Liquid volume flow | 0,5 mL/min to 5 mL/min | 0,06 mL/min | ISO 8316:1987 |
| Volume measurements |
| Piston volumetric apparatuses (pipettes, burettes, dilutors, dispensers) | (1 μL to 2 μL] | 2,0 % to 1,3 % | EN ISO 8655.06:2022 |
|  | (2μL to 10 μL] | 1,3 % to 0,56 % |  |
|  | (10 μL to 100 μL] | 0,56 % to 0,20 % |  |
|  | (100 μL to 1000 μL] | 0,20 % to 0,14 % |  |
|  | (1 mL to 5 mL] | 0,14 % |  |
|  | (5 mL to 10 mL] | 0,13 % |  |
|  | (10 mL to 150 mL] | 0,12 % |  |
| Temperature measurements |
| Climatic and isothermal chambers, Incubators & laboratory ovens, Refrigerators, Cooling chambers with internal volume up to 2000 l, with or without air circulation | [-80 oC to -60 oC] | 0,3 oC | DKD-R 5-7:2018 ELOT ΕΝ 60068-3-5:2018 using Pt100 thermometers and type K thermocouples (for temperature > 250 oC). Calibration is performed on site. |
|  | (-60 oC to 120 oC] | 0,2 oC |  |
|  | (120 oC to 250 oC] | 1,2 oC |  |
|  | (250 oC to 350 oC] | 3,0 oC |  |
| Climatic and isothermal chambers, Incubators & laboratory ovens, Refrigerators, Cooling chambers with internal volume up to 2000 l, with air circulation | [350 oC to 500 oC] | 3,0 oC | DKD-R 5-7:2018 ELOT ΕΝ 60068-3-5:2018 using type K thermocouples. Calibration is performed on site. |
|  | (500 oC to 1000 oC] | 3,0 oC to 3,5 oC | Internal method ΜΔ.06.Θ based on: DKD-R 5-7:2018 ΕΛΟΤ ΕΝ 60068-3-5:2018 EURAMET cg-20 v.5.0:2017 using type K thermocouples. Calibration is performed on site. |
| GC ovens | [-20 oC to 120 oC] | 0,2 oC | DKD-R 5-7: 2018 using Pt100 thermometers. Calibration is performed on site. |
|  | (120 oC to 250 oC] | 1,2 oC |  |
| HPLC ovens | 0 oC to 80 oC | 0,2 oC | DKD-R 5-7: 2018 using Pt100 thermometers. Calibration is performed on site. |
| Autoclaves | 100 oC to 140 oC | 0,3 oC | BS 2646-5: 1993 DKD-R 5-7: 2018 using data loggers. Calibration is performed on site. |
| Liquid baths | -40 oC to +140 oC | 0,4 oC | ASTM E 715: 80 (R2022) DKD-R 5-7: 2018 using data loggers. Calibration is performed on site. |
| Dissolution testers and disintegration testers | 30 oC to 50 oC | 0,3 oC | ASTM E 715: 80 (R2022) using data loggers. Calibration is performed on site. |
| Analog, digital thermometers of direct reading, temperature data loggers | [-80 oC to -40 oC] | 0,8 oC | COFRAC LAB GTA 08: 2017 |
|  | (-40 oC to 75 oC] | 0,09 oC |  |
|  | (75 oC to 125 oC] | 0,11 oC |  |
|  | (125 oC to 600 oC] | 1,1 oC |  |
| Air temperature thermometers | -20 oC to +60 oC | 0,6 oC | COFRAC LAB GTA 08: 2017 |
| Liquid-in-glass thermometer (total / partial immersion) | [-40 oC to 25 oC] | 0,09 oC | COFRAC LAB GTA 08: 2017 |
|  | (25 oC to 125 oC] | 0,11 oC |  |
| Temperature dry block calibrators | [-50 oC to 240 oC] | 0,2 oC | EURAMET cg-13 v.4.0:2017 using Pt100 thermometers. |
|  | (240 oC to 600 oC] | 1,3 oC |  |
| Relative humidity measurements |
| Relative humidity/ Controlled relative humidity chambers, with volume up to 2000 l (Climatic chambers) | 65 %rh (at 30 οC) | 2,5 %rh | DKD-R 5-7:2018 Calibration is performed on site. |
|  | 60 %rh (at 25 οC) | 2,3 %rh |  |
|  | 75 %rh (at 40 οC) | 2,7 %rh |  |
| Relative humidity / Analog and digital hygrometers | [20 %rh to 40 %rh] (40 %rh to 60 %rh) [60 %rh to 90 %rh] at 25οC | 1,7 %rh 1,6 %rh 2,2 %rh | Internal method ΜΔ-16.E based on NPL guideline, “A guide to the measurement of humidity”:1996 using standard hygrometer and climatic chamber. |
|  | [20 %rh to 40 %rh] (40 %rh to 60 %rh) [60 %rh to 90 %rh] At 30οC | 1,9 %rh 1,7 %rh 2,0 %rh |  |
|  | [20 %rh to 40 %rh] (40 %rh to 60 %rh) [60 %rh to 90 %rh] at 40οC | 1,8 %rh 1,7 %rh 2,0 %rh |  |
| Pressure measurements |
| Analog and digital gas medium gauge pressure measuring instruments of direct reading | [10 mbar to 70 mbar) | 0,02 mbar | DKD-R 6-1 v.3:2014 |
|  | [70 mbar to 20 bar] | 5,2 mbar |  |
|  | [-730 mbar to -70 mbar] | 4,5 mbar |  |
|  | (-70 mbar to -10 mbar] | 0,021 mbar |  |

*	Where the expanded uncertainty (with coverage probability 95 %) is accompanied by the corresponding unit, it is absolute, while where it is not accompanied by a unit, it is relative.

** Uncertainty values were estimated assuming a spectrophotometer having a resolution of 0,1 mAU.

The Calibration & Measurement Capability (CMC) includes the measurand, the measurement range and the measurement uncertainty and expresses the smallest measurement uncertainty that can be achieved in a calibration.

Site of assessment: Permanent laboratory premises, 197, Spaton Avenue, GR-153 51 Pallini, Attiki, Greece.

Approved signatories: Gerasimos Mineschos.

This Scope of Accreditation replaces the previous one dated October 4th, 2023.

The Accreditation Certificate No. 388-5, to ELOT EN ISO/IEC 17025: 2017, is valid until 09.10.2028.

Athens, March 15th, 2024

Christos Nestoras

CEO of ESYD