Hellenic Accreditation System

| Annex F1/9 to the Certificate No. 763-4 SCOPE of ACCREDITATION of the Testing Laboratory of the Chemistry Department of the Water Supply & Sewerage Company of Municipality of Sparti |
| --- |
| Materials / Products tested | Types of test / Properties measured | Applied methods / Techniques used |
| Chemical Tests |
| 1. Water-wastes | 1. Determination of pH | APHA 4500-H+ B |
|  | 2. Determination of conductivity | APHA2510 |
|  | 3. Determination of ΝΟ3- | APHA 45000-NO3- B |
|  | 4. Determination of ΝΗ4+, | Dr.Lange LCK304 |
|  | 5. Determination of turbidity | Internal method based on APHA 2130 |
| 2. Water | 1. Determination of Fe, Mn, Cr, Ni, Cu | ISO 11885:2007 |
|  | 2. Determination of Cl- | Internal method based on APHA 4500-Cl E |
|  | 3. Determination of SO42- | Internal method based on APHA 4500-SO4 Ε |
|  | 4. Determination of N-NO2 | Internal method based on APHA 4500-NO2 B |
| 3. Wastes | 1. Determination of COD | Dr.Lange LCK314 |
|  | 2.Determination of Total Nitrogen | Dr.Lange LCK138 |
|  | 3. Determination of Total Phosphorus | Dr.Lange LCK348 & LCK 350 |
|  | 4. Determination of total suspended solids | ELOT EN 872:2005 |

Site of assessement: Permanent laboratory premises – 52 Gortsologlou str. 23100, Sparti, Greece

Approved signatories: G. Lazaras

This scope of Accreditation replaces the previous one, dated 17.07.2023.

The Accreditation Certificate No. 763-4, according to ELOT EN ISO/IEC 17025:2017, is valid until 28.07.2028.

Athens, 9th of January 2024

Christos Nestoras

CEO of ESYD